## Slide 1
Ghana Transportation Incident
Jan 20, 2022
Victoria, April 25-27, 2022

## Slide 2: Ghana Incident review – Jan 20, 2022
https://www.africanews.com/embed/1812046

## Slide 4
Extract from news reports

## Slide 5
Corrective actions taken by the Ghana Government:
Ban on ANFO transportation on a public road to a mine or civil work site unless expressly permitted by the Chief Inspector of Mines.
Explosives guarded by two escort vehicles, one in front and one at the back, both having sirens to warn people about the explosives.
Chief Inspector of Mines notification of their intention to transport explosives 48 hours before the scheduled transportation.
The 14 measures apply fully to all companies involved in manufacturing, supply, transportation, and use of explosives.

## Slide 6
Potential root causes and learnings for the Industry :
Insufficient explosives hazards awareness;
Inadequate emergency response and evacuation procedures;
Road safety challenges. Ghana recorded 73 deaths per 1000 collision, making it the second highest road traffic collision prone nation among six West African countries. (US : ~6 deaths/1000 collision); Ghana: 443 deaths/100,000 vehicles. vs .8.9 deaths/100,000 vehicles. – Canada;
Emergency communication challenges.

## Slide 7
Canadian Emergency Response Guidelines 2020

## Slide 8
Frequency of transportation explosion incidents per product type

## Slide 9
Information Noel Hsu – Orica

## Slide 10
*Information Noel Hsu – Orica

## Slide 11
*Information Noel Hsu – Orica
Truck 2004-06-14 Russia ANE Explosion.
MMU 2006-09-15 USA, ASARCO Ray Pit copper mine. ANE Explosion.

## Slide 12
What is our 50 %
Explosives transport routes planning
Emergency response simulations & emergency communications systems testing.
Explosives hazards training including evacuation procedures and when it is considered safe to fight fires
Fire suppression systems & fire extinguishers.
Proper truck maintenance (tires, breaks, engines, etc.)
Ensure the truck driver is aware of how to activate the ERAP plan in case of incident.
Driver’s fatigue management program.