## Slide 1: Tribunal Hearing on Safety of Mucking under Loaded Holes in Long Hole Mining
Presentation to CEAEC November 2018
Chris Watson/Joey Viljoen

## Slide 2: Long Hole Mining
The long blasthole mining method, “LBH – Large Blasthole” is a form of open pit bench blasting adapted for underground mining operations. Vertical Crater Retreat (VCR) or mechanical raise boring is used to open a slot raise thus creating a vertical free face for the subsequent bench blasting operations. The drilling and mucking operations are carried out on two sublevels; the drilling and loading (explosives) level above and the extraction (mucking) level below.
VCR, also called vertical retreat mining, is a well-established underground mining technique, developed in Canada the 1960s and may be used in certain cases in lieu or in conjunction with the “LBH”. Both methods involve drilling large-diameter holes into the orebody vertically from the top, as opposed to the conventional blasthole stope method of drilling them in fans with upward and/or downward fans.

## Slide 3: Long Hole Mining

## Slide 4: Long Hole Mining
LBH” and/or “VCR” are beneficial mining methods because they reduce the cost of mining orebodies that are wide and steep. They also eliminate the need for a support system after the blasting occurs and increase mining safety because miners do not have to be in the area of the ore when blasting is taking place.
In the operation considered here, mucking is carried out under loaded holes, some of which may be plugged breakthrough holes. This significantly increases the efficiency of the operation.
Miners are not present during the mucking operation, which is carried out by a remotely operated scooptram (LDH vehicle).

## Slide 5: Issues raised by the CNESST
Mucking under loaded holes has been carried out routinely in Quebec and elsewhere without problems for many years. Nevertheless in 2014 the CNESST (Quebec Work Standards, Health and Safety Commission) informed the QMA (Quebec Mining Association) of their intention to prohibit this practice. Several mines presented the CNESST with risk analyses to demonstrate the safety of the method. Reports by Ken Liu and Chris Watson refuting the CNESST objections were presented to the CNESST at a meeting in August 2016. The CNESST attendees asked no questions and made no comments.
Shortly afterwards, the CNESST confirmed their ban on the method, citing inadequate evidence of safety. The CNESST objection to the practice of mucking under loaded holes was that it could lead to an accidental detonation of one or more holes with risk to the miners overhead or on the mucking level.

## Slide 6: Potential Hazard Scenarios provided by the CNESST
A fall of rock causing explosives to fall from a loaded hole onto or near the scooptram (LHD vehicle)
Fall of explosives on a hot part of the scooptram
Impact or friction on explosives caused by scooptram
A fire on the scooptram causing detonation of an overhead hole
Impact by the scooptram on the rock face near a loaded hole
Accidental detonation of a hole during mucking
Impact or friction by scooptram on explosives in muckpile
Detonation of booster assembly hanging from hole caused by impact of scooptram

## Slide 7: Industrial Tribunal Hearing
In 2016 the QMA appealed the CNESST decision to a tribunal hearing, which could confirm or overturn the ban.
Both sides were represented by legal counsel.
The QMA presented expert witnesses on mining, explosives and rock properties to contest the validity of the CNESST assertions.
The CNESST depended mainly on documents produced by the IME and ISEE, and explosives manufacturer’s Safety Data Sheets (SDSs).

## Slide 8: Evidence presented by the CNESST
  The CNESST in large part justified their ban on mucking under loaded holes, or mucking while loading holes on the basis that it was not safe to do so because of the hazards presented by the explosives used
  They used the following sources to support their argument:
    IME SLP 4 (2012 version)
    ISEE – Blaster’s handbook, 18th Edition – Appendix C, “Warnings and Instructions” (were called “Always” and “Never” in older editions)
    Information contained in the SDSs for the relevant explosives

## Slide 9: IME SLP 4 and ISEE Appendix C
  From both sources similar points were used as evidence of explosives hazards:
  NEVER fight fires involving explosive materials. Remove yourself and all other personnel to a safe location and guard the area.
  NEVER expose explosive materials to sources of heat exceeding 150°C (65°C) or to open flame, unless such materials or procedures for their use, have been recommended for such exposure by the manufacturer
  NEVER strike explosive materials with, or allow them to be hit by , objects other than those required in loading
  NEVER subject explosive materials to excessive impact or friction

## Slide 10: SDSs
Section 10 (Stability and Reactivity) presented as evidence regarding sensitivity of explosives products
Emulsion
  Chemical Stability: Extreme risk of explosion by shock, friction, fire or other sources of ignition.
  Conditions to Avoid: Keep away from open flames, hot surfaces and sources of ignition.
ANFO:
  Conditions to Avoid: Keep away from open flames, hot surfaces and sources of ignition. Incompatible materials. Direct sunlight, extremely high or low temperatures, ignition sources, combustible materials, incompatible materials.
  Incompatible Materials: Combustibles, heat sources

## Slide 11: SDSs
Boosters
  Chemical Stability: Stable up to approximately 70°C (158°F). PETN explodes at 190-210°C (374-410°F).
  Conditions to Avoid: Keep away from open flames, hot surfaces, sources of ignition. Extreme risk of explosion by shock or friction.
Detonator Assemblies
  Chemical Stability: Extreme risk of explosion by shock, friction, fire or other sources of ignition. Stable up to approximately 70°C (158 °F).

## Slide 12: Counter arguments
No use in voicing our opinions that some of these statements exaggerated the hazards or were incorrect. We decided that the best route would be to present facts:
    Review history of IME SLP 4 and ISEE Appendix C
    Review the tests required for classification for transportation
    Present some of the tests done by companies on explosive raw materials and products

## Slide 13: Counter arguments
  We also had to explain to the judge what factors affected the behaviour of an explosive, and how these factors differed for different types of explosives
    Critical diameter
    Confinement
    Gap sensitivity
We further needed to explain how packaging explosives into articles changed the explosive properties

## Slide 14: IME SLP 4 and ISEE Appendix C
ISEE Blaster’s Handbook 18th Ed. Appendix C based on IME SLP 4
Chris contacted IME (Deb Satkowiak) for historical versions of the IME SLP 4
“Don’ts” predates 1951, covered High Explosives, Black Blasting Powder, Pellet Powder, Blasting Caps at the time
Became “Do’s and Don’ts” in 1955
Became SLP 4 ca. 1970 – by then included Non-electric detonator assemblies, Detonating cord, blasting agents and water gel slurries and cast boosters

## Slide 15: IME SLP 4 and ISEE Appendix C
The actual “Do’s and Don’ts” were virtually unchanged from the era of dynamite and black powder
They had never been updated with specific sections to deal with ANFO and emulsion
So, although the relative insensitivity of ANFO and emulsion was known to the explosives industry, this information never made it into referenced materials such as these
We have pointed out to the IME that SLP 4 needs review

## Slide 16: Transportation Classification
Reviewed the requirements of UN Tests for the classification of Explosives relevant to the products in question
Test Series 3: These tests determine if a substance (i.e. a powder or liquid) is safe for transportation
  Impact Sensitivity
  Friction Sensitivity
  Thermal stability Test (75°C for 48 hours – substance fails if ignition or explosion occurs)
  Ignition test for response to a fire (Small scale burning test on 10 g sample) –Fails test if sample explodes

## Slide 17: Transportation Classification
Test Series 4: Determines if an article containing explosives is safe for transportation
Noted that many explosives that fail Test Series 3 will pass Test Series 4, since containment and packaging makes them much safer (it practically eliminates friction and protects them against impact).
  Thermal Stability: Article heated at 75°C (167°F) for 48 hours. Fails if it explodes, ignites, experiences a temperature rise of more than 3°C, outer casing or packaging damaged, exudation occurs
  Drop Test: Article or package containing article dropped from a height of 12 m, fails test if an explosion or fire occurs.
(Pointed out that friction tests not done for articles, as containment and packaging of explosives in an article effectively eliminates friction as a hazard).

## Slide 18: Transportation Classification
Test Series 5: Determines if an explosive is a very insensitive explosive with a mass explosive hazard (i.e. it distinguishes between 1.1 and 1.5 explosives).
  Cap Sensitivity Test (Shock test): Determines sensitivity to internal stimulus (shock provided by a standard detonator). Cap sensitive if test material detonates.
  Thermal tests: Determines tendency for Deflagration to Detonation Transition (DDT) - Explosive not classified as 1.5 if detonation occurs.
  External fire test: Determines if a substance, when in large quantities (samples size 200 kg), explodes when subjected to a large fire – Explosive not classified as 1.5 if it explodes.

## Slide 19: Tests by Manufacturers
Emulsions – Bullet tests
Detonators, detonating cord, boosters – Impact tests

## Slide 20: Emulsions sensitivity – impact - Bullet test
As typical impact tests used for explosives do not give positive test results for emulsions, bullet tests used instead
Tests shooting high-velocity projectile (rifle shots) into emulsion contained in a tube have shown that:
  Unsensitised (Division 1.5) emulsion does not detonate
  Sensitized emulsion (Division 1.1) needs a bullet velocity of at least 550-600 m/s to detonate at 20°C
  Bullet has to be shot directly into the emulsion, addition of 6 mm aluminum layer in between is enough to prevent detonation

## Slide 21: Explosives sensitivity & enclosing explosives in an article
Enclosing explosives in an article (e.g. detonator tube, detonating cord) dramatically reduces sensitivity
Having the explosive present in a non-powder form reduces sensitivity (e.g. cast boosters)
Friction virtually eliminated
Impact Sensitivity:
  Enclosure / coatings provide protection
  Impact sensitivity significantly reduced
Heat
  Packaging also provides some protection
  Sufficient heating can result in burning, but unless present in critical diameter will not detonate
  Time to react

## Slide 22: Additional Explosive Properties relevant to use in a Mining Environment
  Critical Diameter
  Confinement
  Gap Sensitivity

## Slide 23: Summary for Critical Diameter and Confinement
Sufficiently large critical diameter + Confined = Sustained Detonation
Critical diameter too small + Confined = NO sustained detonation
Sufficiently large critical diameter + Unconfined = NO sustained detonation

## Slide 24: Gap Sensitivity
Emulsions:
Typically have gap sensitivities from 0 – 13 cm, depending on the degree of sensitization
Emulsion used underground will require contact with the booster for propagation (i.e. has a gap sensitivity of 0 cm)
  Emulsion used underground is partially sensitized, i.e. Division 1.5, not Division 1.1
At distances greater than these distances emulsion will not initiate

## Slide 25: Worst credible event
Risk of ANFO or emulsion detonating due to an impact or heat event vanishingly small – detonation not credible
  Gap to ANFO or emulsion in bottom of hole too great – several meters
  If leaks occur due to improperly plugged hole, the amounts will be too small to detonate upon heating or impact and there will be insufficient amounts present to sustain detonation
Primed booster extending through improperly plugged hole
  Impact likely to shatter it, but small chance of detonation
  Heat may over time lead to a detonation, but will not be instantaneous – i.e. time to react, and will likely just burn due to insufficient confinement
  But detonation of a 454 g primed booster worst credible event

## Slide 26: CERL Magazine trials
The CNESST presented one of the videos of the CERL magazine trial as evidence that if a booster exploded underground the results would be catastrophic.
However:
Chances for damage and injury are clearly fragment driven
Overpressure already under 5 psi at 10 m in all three positions for pressure transducers for the 5 kg
The Lego block barricades used in the second test appeared to be effective for metal sided magazines’ side on debris
The scooptram will likely offer similar protection against secondary rock debris

## Slide 27: Decision of Tribunal
The hearing dragged on interminably due to the stalling tactics of the CNESST lawyers. Finally, in June 2018, the Tribunal’s decision was rendered, in favour of the QMA.
The judge gave a number of reasons:
- There is nothing in the Quebec Regulations which forbids the practice
- The prohibition orders spoke of possible risk, not probable danger
- The inspectors who had issued the prohibition orders to the mines had not even witnessed the operations
- The inspectors relied on information provided for the general public (naturally very conservative) and were not even aware of more detailed and specific information provided by the manufacturers
Overall, the judge was quite critical of the CNESST.

## Slide 28: Lessons for the Explosives Industry
While eventually a favourable judgement was reached, the mining companies lost millions of dollars due to lost production and legal costs.
This was due in part to the inadequate and often misleading SDSs provided by the explosive manufacturers. These appeared in some cases to have been prepared by someone with little knowledge of explosives.
Manufacturers have spent many years and a lot of money developing much safer explosives. While the need to err on the side of caution is recognized, not to acknowledge the safety of modern explosives is to the detriment of both user and producer.
A CNESST lawyer commented that manufacturers were required to provide accurate information on the properties of their products. Could the judge’s rebuke to the CNESST provoke some action by the Commission against the manufacturer?